## Slide 1: OpenBox: A Software-Defined Framework for Developing, Deploying, and Managing Network Functions
Yotam Harchol
The Hebrew University of Jerusalem
Joint work with Anat Bremler-Barr and David Hay
This research was supported by the European Research Council ERC Grant agreement no 259085, the Israeli Centers of Research Excellence (I-CORE) program (Center No. 4/11), and the Neptune Consortium.

## Slide 2: Network Functions (Middleboxes)
Firewall
Load Balancer
Intrusion Prevention System
Monolithic closed black-boxes
  High cost
  Limited provisioning and scalability
Network Function Virtualization (NFV):
  Reduce cost (by moving to software)
  Improve provisioning and scalability (by virtualizing software NFs)
Notes: NFs, or middleboxes, have been traditionally implemented as closed hardware appliances.

## Slide 3: Network Functions (Middleboxes)
High cost
Limited provisioning and scalability
Limited and separate management
  Different vendors
  No standards
  Separate control plane
Notes: However, NFs, virtual or physical, still have other problems

## Slide 4: Network Functions (Middleboxes)
Actually, many of these black-boxes are very modular
Network Function
High cost
Limited provisioning and scalability
Limited and separate management
Limited functionality and limited innovation (High entry barriers)
Similar complex processing steps, no re-use
Notes: high entry barriers – if someone wants to improve or change they need to do everything from scratch

## Slide 5: OpenBox
OpenBox
Controller
OBI
OBI
OBI
OpenBox: A new software-defined framework for network functions
Decouples network function control from their data plane
Unifies data plane of multiple network functions
Benefits:
Easier, unified control
Better performance
Scalability
Flexible deployment
Inter-tenant isolation
Innovation
github.com/OpenBoxProject
www.openboxproject.org
Notes: להתלהב!
OpenBox is a new…
NFs now become applications on top of the OpenBox controller.
The OpenBox data plane realizes the packet processing as directed by the controller.
Packet processing remains in data plane.
The benefits we get are: …
WE IMPLEMENTED

## Slide 6: The OpenBox Framework
Logically-Centralized OpenBox Controller
Network Functions:
OpenBox Applications
Control Plane
Data Plane
OpenBox Service Instances
OpenBox Protocol
Northbound API
Additionally:
Isolation between NFs / multiple tenants
Support for hardware accelerators
Dynamically extend the protocol
Notes: Northbound API to specify NF logic
Logically-centralized controller that unifies logic of multiple network functions from multiple tenants
Communication protocol between controller and data plane
Specification of data plane instances that perform the actual packet processing (packets do not flow through the controller) (ADD EXAMPLE)

## Slide 7: Most network functions do very similar processing steps
Observation:
But there is no re-use…
The design the OpenBox framework is based on this observation

## Slide 8: Network Function Decomposition
Firewall:
Read Packets
Header Classifier
Drop
Alert
Output
Load Balancer:
Read Packets
Header Classifier
Rewrite Header
Output
Intrusion Prevention System:
Read Packets
Header Classifier
Drop
Alert
DPI
DPI
DPI
Output
Notes: We use Click-like notation to decompose NF logic
Each block has its own configuration parameters

## Slide 9: Northbound API
OpenBox Protocol
OpenBox Service Instances
OpenBox
Controller
OpenBox
Applications
Control Plane
Data Plane
NB API
Read Packets
Header Classifier
Drop
Alert
Output
Read Packets
Header Classifier
Rewrite Header
Output
Read Packets
Header Classifier
Drop
Alert
DPI
DPI
DPI
Output
Specify processing graph and block configuration
Events,
Load information
Intrusion Prevention System
Load Balancer
Firewall
Notes: Give example for events and load info

## Slide 10: Logically-Centralized Controller
OpenBox Protocol
OpenBox Service Instances
OpenBox
Controller
OpenBox
Applications
Control Plane
Data Plane
NB API
Multiple tenants run multiple applications for multiple policies in the same network
Isolation between applications and tenants enforced by NB API
SDN Protocol
SDN Switches
SDN
Controller
Network-wide view
Automatic scaling, provisioning, placement, and steering

## Slide 11: Naïve Graph Merge
Firewall:
Read Packets
Header Classifier
Drop
Alert
Output
Intrusion Prevention System:
Read Packets
Header Classifier
Drop
Alert
DPI
DPI
DPI
Output
Header Classifier
Drop
Alert
(IPS)
DPI
DPI
DPI
Output
Read Packets
Header Classifier
Drop
Alert
(Firewall)
Concatenated Processing Graph:
Performance ≈ Diameter of Graph (# of classifiers)
Total: 134μs
30μs
10μs
50μs
10μs
2μs
2μs
30μs
Notes: The performance is correlated with the diameter

## Slide 12: Graph Merge Algorithm
Merged Processing Graph:
Read Packets
Header Classifier
Drop
Alert (IPS)
DPI
DPI
DPI
Output
Alert (Firewall)
Alert (Firewall)
Alert (Firewall)
Alert (Firewall)
Shorter Diameter (less classifiers)
Algorithm and details are in the paper
30μs
10μs
50μs
10μs
Total: 104μs (22% improvement)
2μs
2μs
Notes: In the paper we provide an algorithm that merges multiple processing graphs, and specifically merges classifiers to reduce the lengths of paths in the result graph. We show that this indeed improves data plane performance.
---
It may not always be good to merge, controller can determine when it is good

## Slide 13: OpenBox Data Plane Processing
Read Packets
Header Classifier
DPI
Classification
VLAN Pop
VLAN Push
Rewrite Header
Header Modification
Begin Transaction
Rollback Transaction
Commit Transaction
Transactions
Gzip Decompress
Gzip Compress
De/compression
HTML Normalizer
JavaScript Normalizer
XML Normalizer
Normalization
Store Packet
Restore Packet
Caching
Alert
Log
Reporting
Output
Drop
Terminals
FIFO Queue
Front Drop Queue
RED Queue
Leaky Bucket
Queue Management

## Slide 14: OpenBox Data Plane Processing
OpenBox Service Instance
Virtual or Physical
Provides data plane services to realize the logic of network functions
Controlled by the logically-centralized OpenBox controller

## Slide 15: Distributed Data Plane
OpenBox Service Instance
Software
OpenBox Service Instance
Hardware
(TCAM)
E.g., an OpenFlow switch with encapsulation features
(e.g., NSH, Geneve, FlowTags)
Header Classifier
Alert
DPI
Rewrite Header
Metadata

## Slide 16: Split Processing Graph
Read Packets
Header Classifier
Drop
Output
Write Metadata
Encapsulate Metadata
Read Packets
Drop
Alert
DPI
DPI
DPI
Output
Decapsulate Metadata
Read Metadata
HW Instance:
SW Instance:
Notes: IPS processing graph

## Slide 17: Extensible Data Plane
OpenBox Protocol
OpenBox Service Instances
OpenBox
Controller
Control Plane
Data Plane
NB API
Media Encoder
Option 1:
New hardware implementation
Supports encapsulation
Option 2:
Software module injection
NEW APP
Custom
software module (signed)
On the fly
No need to recompile
No need to redeploy

## Slide 18: Scalable & Reliable Data Plane
OBI
OBI
OBI
OBI
OBI
Scalability
Provisioning
Reliability
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OBI
OpenBox
Controller
Provision
OBI
Hypervisor
Hypervisor

## Slide 19: Implementation
Java-based OpenBox Controller
Software OpenBox Service Instance
Generic wrapper for execution engines (Python)
FW
Northbound API
REST client/server
Graph Aggregator
Management API
Network Manager
Translation Engine
github.com/OpenBoxProject
REST
IPS
Load Balancer
. . .
Click-based execution engine (C++)
Control Plane
Data Plane
REST API
(Plug here other execution engines. E.g., ClickNP)
5500 LoCs
(Python)
2400 LoCs for plugin (C++)
7500 LoCs
(Java)
Notes: Or the one we are working on now which is a hybrid SW-HW using a HW OpenFlow switch

## Slide 20: Performance Improvement
VM1
Firewall
VM2
IPS
Without OpenBox
VM1
OBI1: FW+IPS
VM2
OBI2: FW+IPS
With OpenBox
Chart: Throughput [Mbps]
| Firewall | IPS
Throughput | 840 | 454
Latency | 48 | 76
Standalone VM
Chart: Throughput [Mbps]
Throughput | 454 | 846
Latency | 124 | 80
NF Pipeline
+86%
-35%
Without OpenBox
With OpenBox
Notes: Now for some performance measurments
We consider a simple scenario where packets go from one host through a firewall, then through an IPS, then to another host.

## Slide 21: Conclusions
Network functions are currently a real challenge in large scale networks
OpenBox decouples the data plane processing from network function control logic and:
  Reduces costs
  Enhances performance
  Improves scalability
  Increases reliability
  Provides inter-tenant isolation
  Allows easier innovation
OpenBox Protocol
OpenBox Service Instances
OpenBox
Controller
OpenBox
Applications
Control Plane
Data Plane
NB API

## Slide 22
Limitations

## Slide 23: State Management
Glosses over state management
No Detail about API Implementation
State Replication, latency etc

## Slide 24: Fault Tolerance
State Replication
Traffic Steering
NF Replication

## Slide 25: Implementation
Code is still under development
Incomplete Components
Mininet Implementation does not work

## Slide 26: Further Work
Use P4 to extend the OpenBox system to become protocol agnostic.

## Slide 27
Questions?